## Slide 1
Made possible by grants from the NSF and the Schmidt Foundation
PEARC21
OSN Pod Hardware & Software
July 19, 2021
NSF grants
1747552
1747493
1747507
1747490
1747483

## Slide 2: The Data Deluge
Capture | Store | Share | Analyze

## Slide 3: US Research Cyber-Infrastructure Today
Local, Regional and National Resources
Standardized
Over 200 universities with 40/100Gb Connectivity
Standardized
Largely Balkanized
Many Standards to Choose From
Networking
Storage
Computation

## Slide 4: The Open Storage Network
National resource for sharing open scientific data
Distributed Infrastructure and Governance
Notes: Implementors, please stand up so we can see you!

## Slide 5: The Open Storage Network
National resource for sharing open scientific data
Distributed Infrastructure and Governance
Notes: Implementors, please stand up so we can see you!

## Slide 6: Topics
OSN Pod Hardware and Software Design
OSN Command Center
How to Join the OSN

## Slide 7
OSN Pod Hardware

## Slide 8: OSN Pod Overview
Hardware is deployed in “Scalable Units” known as Pods
Each Pod is:
A single bill of materials
Delivered with all hardware racked and configured
  Sites just need to connect power and networking
Capable of 40Gbps sequential IO
Target cost $150,000
1 PB useable storage (\w 2019 hard drive prices)
Notes: The single bill of materials will include everything needed to run an OSN pod.
The $150,000 cost is just a target because each state has different tax requirements and may need to work with specific VARs.

## Slide 9: Storage Node Highlights
5 Storage Nodes per Pod
4U Supermicro Server
18 Core Skylake CPU
256 GB RAM
36 x 8TB Seagate HDD
2 x 50 GbE data network
5 Node Total: 1.44 PB Raw Storage
Complete Hardware Details at https://www.openstoragenetwork.org

## Slide 10: Proxy Node & Switch Highlights
3 Monitor/Proxy Nodes per Pod
1U Supermicro Server
18 Core Skylake CPU
256 GB RAM
2 x 50 GbE data network
Top of Rack Switches
Mellanox SN2100 16-port 100 GbE
Netgear M4300 24-port 1 GbE

## Slide 11: OSN Pod Benchmarks
IceCube (SDSC) recorded 5.5 GBps read speed from 10 nodes. IceCube only able to get 4 GBps from Azure Storage and AWS S3 in similar tests.
Pangeo (NCSA) was “extremely impressed” with the results of their benchmarks. Pangeo achieved 5.5 GBps read speeds from threaded tests. They reported higher throughput from the OSN than from Google’s Cloud Storage US-CENTRAL region. “OSN is a very viable alternative to cloud storage for us for many use cases” - Pangeo
Notes: IceCube - The IceCube Neutrino Observatory - https://icecube.wisc.edu
Pangio - A community platform for Big Data geoscience - https://pangeo.io

## Slide 12: Possible OSN Pod Updates for 2022+
High Redundancy Full Rack Pod:
12 Nodes
  2U Servers
  SSD/NVMe for Cache/Journal
Same rack, power, and networking requirements
Single Server Pod:
4U 90 disk bay server
For locations with physical size limitations
Still 1 PB of usable storage and target cost of $150,000

## Slide 13
OSN Pod Software

## Slide 14: What is Ceph?
Open source distributed object storage service
S3 Compatible Object Storage
Block Storage
POSIX-Compatible File System
Ink Tank released first stable version of Ceph in 2012
Red Hat purchased Ink Tank in 2014
Red Hat Ceph Storage (RHCS) - Licensed
Community Supported - Free

## Slide 15: Ceph at the OSN
Currently running the community supported version
Only the S3 compatible Object Storage service
Running version 14.2 (Nautilus)
Using ceph-ansible for configuration management

## Slide 16: Supported S3 Features
Ceph supports a RESTful API that is compatible with the basic data access model of the Amazon S3 API.
More Details at https://docs.ceph.com/en/latest/radosgw/s3/
List Buckets | Bucket ACLs (Get, Put) | Put Object | Copy Object
Delete Bucket | Bucket Location | Delete Object | Multipart Uploads
Create Bucket | Bucket Notification | Get Object | Object Tagging
Bucket Lifecycle | Bucket Object Versions | Object ACLs (Get, Put) | Bucket Tagging
Policy (Buckets, Objects) | Get Bucket Info (HEAD) | Get Object Info (HEAD) | Storage Class
Bucket Website | Bucket Request Payment | POST Object | 
S3 Compatible

## Slide 17: OSN Pod Durability
Assumptions:
0.44% Annual Failure Rate Reported by Seagate
Failed disk removed within 1 day of failure
https://github.com/Backblaze/erasure-coding-durability
Erasure Code Profile | Durability
3+1 (OSN First Gen) | 99.9999% (6 9s)
4+2 (OSN Future) | 99.99999999% (10 9s)
AWS S3 Standard | 99.999999999% (11 9s)
8+3 (OSN Future) | 99.999999999999% (14 9s)
Notes: For example, if you store 10,000,000 objects, you can on average expect to incur a loss of a single object once every 1,000 years.
Amazon S3 Standard has 11 9s of durability

## Slide 18: OSN Pod Space Reservations
Ceph Overhead - Disks won’t fill past 95%.
Ceph Metadata - Space reserved for information about objects and accounts.
Reserved Space - Space reserved for node failure. This space is only allocated to projects if the project cannot be allocated on another Pod.
Allocatable Space - Space available to projects.

## Slide 19: Future OSN Ceph Updates
Plans to upgrade to Ceph 16.2 (Pacific) in 2021
Switch from ceph-ansible to cephadm for Ceph deployment and management
  ceph-ansible too slow to deploy small changes
  Prone to failures when disks fail
  Will keep using Ansible for managing other software on the pods

## Slide 20
OSN Command Center

## Slide 21: OSN Command Center
Collection of services hosted on servers at MGHPCC and JHU
  Pod provisioning and Software Install/Update
    Bootstrap - Bare metal to functioning storage appliance
    Software install/updates - Ongoing Ceph and community software distribution
  Monitoring and Alerting
    Telegraf, Influx, Grafana (TIG) stack, Slack
  Web Applications
    Storage Portal
    Website

## Slide 22: OSN Command Center
Collection of services hosted on servers at MGHPCC and JHU
  Pod provisioning and Software Install/Update
    Bootstrap - Bare metal to functioning storage appliance
    Software install/updates - Ongoing Ceph and community software distribution
  Monitoring and Alerting
    Telegraf, Influx, Grafana (TIG) stack, Slack
  Web Applications
    Storage Portal
    Website

## Slide 23: Pod provisioning and Software Install/Update
Bootstrap, software install, lifecycle

## Slide 24: Provisioning - Bootstrap
Command Center (Provisioning)
ctl01.osn.xsede.org
ctl02.osn.xsede.org
mon01
mon03
dat01
dat02
dat03
dat04
dat05
GitHub
Gateway
Download Latest Config
ssh
IPMI
mon02
Command Center – OSN Admin
Bootstrap nodes via ansible from command center
  Configs pulled from project GitHub repo
  Images pushed to gateway node
  IPMI / PXE used to bootstrap remaining nodes

## Slide 25: Provisioning - System
mon01
mon03
dat01
dat02
dat03
dat04
dat05
GitHub
Gateway
Command Center (Provisioning)
ctl01.osn.xsede.org
ctl02.osn.xsede.org
Download Latest Config
ssh
SSH/Ansible
Package installation
routing
Switch configuration
Firewall/Iptables
Etc.
Etc.
Command Center – OSN Admin
Bootstrap nodes via ansible from command center
  Configs pulled from project GitHub repo
  Images pushed to gateway node
  IPMI / PXE used to bootstrap remaining nodes
Execute baseline system services installation
mon02
OSN Package Repo
https

## Slide 26: Provisioning - Software
GitHub
Command Center (Provisioning)
ctl01.osn.xsede.org
ctl02.osn.xsede.org
Download Latest Config
ssh
SSH/Ansible
Etc.
Etc.
mon01
mon02
mon03
dat01
dat02
dat03
dat04
dat05
RGW
iRods
Etc.
Ceph / Radosgw
iRODS
Command Center – OSN Admin
Bootstrap nodes via ansible from command center
  Configs pulled from project GitHub repo
  Images pushed to gateway node
  IPMI / PXE used to bootstrap remaining nodes
Execute baseline system services installation
Provision Software
  storage system (Ceph)
  User service stack (Rgw, iRods, etc.)
OSN Package Repo
https

## Slide 27: Lifecycle: Software Configuration and Maintenance
Developer checks out a bugfix/feature branch
Modify, debug, and test locally
Trial deployment on a single pod
Implementation team review and and approval
Branch is merged to main branch for deployment in next update
GitHub
Local Test HW/VMs
Branch
Review/merge
Release
Candidate
Validate
Release
Release
Test/Staging
Community Development
Develop
Test
OSN
Sites
Command Center

## Slide 28: Monitoring and Alerting

## Slide 29: Monitoring - Telegraf, InfluxDb, Grafana
Dashboard
Pod Hardware
Pod Ceph

## Slide 30: Alerting - Slack

## Slide 31: Web Applications
Storage Portal and Website

## Slide 32: Storage Portal - Architecture
Four User Communities:
End User
Data Manager
Data Curator
OSN Administrator

## Slide 33: Storage Portal- End User / Key Distribution

## Slide 34: Storage Portal - End User Data Access
Built-in Object Browser
Cloud Storage GUI Client
Cloud Storage Command Line Client

## Slide 35: Storage Portal - Datamanager

## Slide 36: Storage Portal - Data Curator
Landing Page Editor
Landing Page

## Slide 37: Storage Portal - OSN Administrator (Manual)
Create Projects
Assign Datamanagers to projects
Create/Assign buckets to projects
Manage buckets

## Slide 38: Storage Portal - OSN Administrator (XSEDE)

## Slide 39: Website

## Slide 40: Adding Data Sets | Becoming an OSN Storage Site

## Slide 41: A Few Simple Ideas
• Collaborative Governance and Operation
• Geographically distributed Storage, accessible via URIs
Centralized management where needed for cost effective operation

## Slide 42: Adding a Data set to the OSN
• Up to ~10 Terabytes • XSEDE startup allocation (applications reviewed when received)
• Up to ~100 Terabytes • XSEDE Research allocation (applications reviewed quarterly)
• More than ~100 Terabytes • Work with OSN to obtain funding for new capacity

## Slide 43: Adding Capacity to the OSN
• Host OSN storage • In cooperation with other OSN members
• Participate in governance and/or operation • advisory board | leadership team | devops team

## Slide 44: Hosting OSN Storage – General Considerations
• Network Access • Locate pods in a Science DMZ, with access to Internet2
• Security • Sites are responsible for physical access control and network security outside the pod • OSN Pods follow Trusted CI Center of Excellence guidelines
• Software Installation and Maintenance • Supported by the Command Center
• Hardware Acquisition, Installation, and Maintenance • See next slide

## Slide 45: Hardware Acquisition, Installation, and Maintenance
• Option 1 - Install an OSN Pod • Single rack of equipment, fully integrated prior to delivery • Hardware failures detected by the Command Center • Site staff needed for hardware replacement
• Option 2 (in development) - Leverage Existing Storage • Assign a slice of an existing storage system to the OSN • Install an OSN gateway that supports: • Access to the storage via OSN URIs • Management of the storage via the OSN Command Center

## Slide 46: Questions
Jim Culbert
Director of IT Services
MGHPCC culbertj@mghpcc.org
Kevin Coakley
Senior Storage Systems Engineer
SDSC kcoakley@sdsc.edu
John Goodhue
Executive Director
MGHPCC jtgoodhue@mghpcc.org